## Slide 1
LINGLONG SG98
New Motor Backend Implementation Template
A copy-and-fill playbook for adding a new RS-485 motor family by replacing only the motor-specific commands.
Keep RT shape. Replace only the motor-specific blocks.
Primary source: Documentation/New-Motor-Backend-Implementation-Template.md
Notes: Set the expectation: this is the practical follow-on to the overview guide and is meant to be used while editing code.
[Sources]
- Documentation/New-Motor-Backend-Implementation-Template.md
- Documentation/New-Motor-Backend-Guide.md
- src/RT/motorcontrol_rt.h and src/RT/motorcontrol_rt.cpp

## Slide 2
WORKING MODEL
02 / 10
Copy RT And Keep The Shape
The fastest path is to preserve the existing loop structure and only swap the drive-specific register logic.
Keep
Disconnect handling, comm
health checks, state
updates, send and receive
flow, and the split between
connect, run, stop, and
polling.
Replace
Probe register, setup
writes, forward and reverse
commands, telemetry decode,
stop path, sleep path, and
optional reset path.
Use JMC only when needed
Switch to the JMC backend as
your template only when you
need multi-baud probing or a
more stateful enable
sequence.
Template starting point: src/RT/motorcontrol_rt.cpp
Notes: This slide should lower the cognitive load: do not design a new framework, just reuse the RT backend shape.
[Sources]
- Documentation/New-Motor-Backend-Implementation-Template.md
- src/RT/motorcontrol_rt.h and src/RT/motorcontrol_rt.cpp
- src/JMC/motorcontrol_jmc.h and src/JMC/motorcontrol_jmc.cpp

## Slide 3
INPUTS
03 / 10
Collect These Manual Facts Before Coding
The backend goes quickly once the safe registers and command model are known.
Bus
Baud, parity, stop bits,
slave ID rules, and whether
the drive boots in a
predictable profile.
Control
Enable, disable, run, stop,
direction, speed, torque,
ramp, save, sleep, and reset
commands.
Telemetry
Status, actual RPM, actual
torque or load, and a fault
register that can be trusted
during bench testing.
If the worksheet is incomplete, stop and get the missing manual data first
Notes: Call out that missing manual facts are the biggest source of wasted bring-up time.
[Sources]
- Documentation/New-Motor-Backend-Implementation-Template.md

## Slide 4
TRANSPORT
04 / 10
Know Which Comm Helper To Use
The transport layer is already done. The main choice is whether the command is blocking bring-up work or async runtime traffic.
Blocking helpers
Use writeConfirm,
writeMultipleConfirm, and
readReturn for probe,
one-time setup, off, sleep,
and reset.
Async sends
Use writeSingleRegister,
writeMultipleRegisters, and
readRegister inside tick for
the live comm loop.
Receive path
Call receive in tick, then
decode lastRequestType and
lastRead so the backend
updates cached mirrors and
live telemetry.
Transport truth: src/comm.cpp
Notes: This is where people usually overcomplicate things. Stress that the transport layer is already the shared abstraction.
[Sources]
- Documentation/New-Motor-Backend-Implementation-Template.md
- src/comm.h and src/comm.cpp

## Slide 5
FILE SETUP
05 / 10
Top Of File: Registers, Mirrors, And Probe
Start the new backend by declaring readable constants and local register mirrors instead of editing the RT numbers in place.
Constants
Add FOO_REG_STATUS,
FOO_REG_RPM, FOO_REG_TORQUE,
enable, direction, ramp,
fault, and any split forward
or reverse speed registers.
Mirrors
Keep confirmed reg_* mirrors
and pending_reg_* values for
async multi-register writes
so tick knows what still
needs to be sent.
Probe helper
Build a tiny probe around
motor_probe_set_profile plus
motor_probe_read_register,
and make it specific enough
that it cannot lie.
Use readable names tied to motor function, not recycled RT register numbers
Notes: The key message is to rename things to the new motor semantics immediately so the file stays maintainable.
[Sources]
- Documentation/New-Motor-Backend-Implementation-Template.md
- src/motor_probe.h and src/motor_probe.cpp
- src/RT/motorcontrol_rt.h and src/RT/motorcontrol_rt.cpp

## Slide 6
HOOKS
06 / 10
Fill Probe, Init, And Connect-Time Setup
init should only clear local state. The actual drive setup belongs in the first connected branch inside tick.
probe
Return true only when a
distinctive status block
really answers. For
multi-baud families, follow
the JMC try-and-restore
pattern.
init
Reset motor_setRPM, live
readback, commStatus,
currentStatus, and every
cached reg_* mirror. Keep
init lightweight.
First connection
Inside the commStatus ==
COMM_DISCONNECTED branch,
send one-time mode, source,
ramp, or save writes that
must happen once per
connection.
Heavy setup goes in the connect-time branch, not in init()
Notes: This slide explains the most important architectural placement rule in the implementation template.
[Sources]
- Documentation/New-Motor-Backend-Implementation-Template.md
- src/JMC/motorcontrol_jmc.h and src/JMC/motorcontrol_jmc.cpp
- src/RT/motorcontrol_rt.h and src/RT/motorcontrol_rt.cpp

## Slide 7
TICK LOOP
07 / 10
The Tick Function Has Four Replaceable Blocks
The send and receive loop already has a good shape. Most ports only need to replace the motor-specific logic inside each block.
Receive decode
Decode write
acknowledgements, read
responses, and optional
multi-write responses.
Update reg_* mirrors,
currentStatus,
motor_currentRPM, and
motor_currentTorque.
Stop branch
When effectiveSetRPM is
zero, write the drive to a
safe stopped state in the
exact order the manual
expects, then switch into
polling.
Run branches
Mirror the same pattern for
forward and reverse: set
enable, torque, speed, and
direction or jog mode, then
poll once the drive is
settled.
Keep the loop shape. Swap only the motor-specific commands and register decode
Notes: The biggest failure mode is rewriting tick from scratch. The deck should push people away from that.
[Sources]
- Documentation/New-Motor-Backend-Implementation-Template.md
- src/RT/motorcontrol_rt.h and src/RT/motorcontrol_rt.cpp
- src/JMC/motorcontrol_jmc.h and src/JMC/motorcontrol_jmc.cpp

## Slide 8
COMMANDS
08 / 10
Choose The Right Command Pattern
Most new motors fit one of three models: split forward and reverse speed registers, absolute speed plus direction, or absolute speed plus signed torque.
RT style
Forward speed and reverse
speed are separate
registers. Forward writes
speed_fwd, reverse writes
speed_rev, and jog mode
selects direction.
Direction register style
The drive wants one absolute
speed register and a
separate direction value.
Forward and reverse both set
the same speed register.
Signed torque style
The drive uses one absolute
speed register but torque or
command polarity determines
the real direction, similar
to the JMC path.
Pick the model that matches the manual, then keep forward and reverse logic symmetric
Notes: This slide helps people classify the new drive before they start editing forward and reverse branches.
[Sources]
- Documentation/New-Motor-Backend-Implementation-Template.md
- src/RT/motorcontrol_rt.h and src/RT/motorcontrol_rt.cpp
- src/JMC/motorcontrol_jmc.h and src/JMC/motorcontrol_jmc.cpp

## Slide 9
REGISTRATION
09 / 10
Wire The Backend Into Motor HAL
Once the new file compiles, the rest is table work: DriveType, probe report fields, command descriptors, and the MotorDescriptor entry.
DriveType
Add DRIVE_TYPE_FOO in
src/motor_hal.h and only the
MotorProbeReport fields
needed to explain what the
probe matched.
Command table
Define FOO_COMMANDS with
menuNum, itemIdx,
valueScale, supported, and
help text. Mark unsupported
controls honestly.
MotorDescriptor
Register key, label,
commProfile, maxRpm,
torquePercentNumerator,
probePriority, commands, and
MOTOR_BACKEND_FOO.
Shared registration lives in src/motor_hal.h and src/motor_hal.cpp
Notes: This slide connects the backend file to the shared auto-detect and menu system.
[Sources]
- Documentation/New-Motor-Backend-Implementation-Template.md
- src/motor_hal.h and src/motor_hal.cpp

## Slide 10
SCALE + TEST
10 / 10
Finish With Scaling And Bring-Up Order
Most bugs after the first spin are not architecture bugs. They are usually command scaling, torque decode, or test-order mistakes.
Scaling
Use valueScale to turn UI
values into drive units.
Start by copying the closest
existing backend, then
bench-check displayed torque
percent.
Comm profile
Add a new CommProfile only
if baud, parity, stop bits,
or timing truly differ.
Otherwise reuse the closest
existing profile.
Bench order
Compile, probe, off, status,
RPM readback, forward run,
reverse run, torque, then
optional ramp, save, sleep,
and reset.
Lowest-risk rule: make off() work before you chase full-speed run control
Notes: Close on sequencing: safety and observability first, then full control.
[Sources]
- Documentation/New-Motor-Backend-Implementation-Template.md
- src/comm.h and src/comm.cpp
- src/motor_hal.h and src/motor_hal.cpp